Series Wheel Aligner Service and Parts Manual

# Trademark Information

PROTEC is a being registered trademark of Protec Equipment Canada in Canada. All other PROTEC trademarks, service marks, domain names, logos, and company names referred to in this manual are either trademarks, registered trademarks, service marks, domain names, logos, company names of or are otherwise the property of Protec Equipment Canada or its affiliates. In countries where any of the PROTEC trademarks, service marks, domain names, logos and company names are not registered, Protec Equipment Canada claims other rights associated with unregistered trademarks, service marks, domain names, logos, and company names. Other products or company names referred to in this manual may be trademarks of their respective owners. You may not use any trademark, service mark, domain name, logo, or company name of Protec Equipment Canada or any third party without permission from the owner of the applicable trademark, service mark, domain name, logo, or company name. You may contact Protec Equipment Canada by visiting us at our website, to request written permission to use Materials on this manual for purposes or for all other questions relating to this manual.

# Copyright Information

All rights reserved by Protec Equipment Canada. No part of this publication may be reproduced, stored in a retrieval system, or transmitted in any form or by any means, electronic, mechanical, photocopying, recording or otherwise, without the prior written permission of Protec Equipment Canada. The information contained herein is designed only for the use of this unit. Protec Equipment Canada is not responsible for any use of this information as applied to other units.

Neither Protec Equipment Canada nor its affiliates shall be liable to the purchaser of this unit or third parties for damages, losses, costs, or expenses incurred by purchaser or third parties as a result of: accident, misuse, or abuse of this unit, or unauthorized modifications, repairs, or alterations to this unit, or failure to strictly comply with Protec Equipment Canada operating and maintenance instructions.

Protec Equipment Canada shall not be liable for any damages or problems arising from the use of any options or any consumable products other than those designated as Original Protec Equipment Canada Products.

# Precautions

- Please read the User’s Manual and the Installation and Parts Manual carefully before operating Ultra3D.

- Only the qualified technician can operate the Wheel Aligner.

- The operator must have knowledge of computer application and basic theory of wheel alignment.

- The power voltage of Ultra3D is AC110~240V±10% 50±1Hz / 60±1Hz. The power outlet must be a Three PIN socket and its earth pin must be well grounded. If the power voltage is not stable, please purchase and use AC voltage stabilizer.

- Ultra3D is operated with image sensing; by analyze target images recorded by high-resolution video camera. Avoid reflect Infrared light or direct sun light to the targets.

- Ultra3D is high precision equipment; special care should be taken during installation and operation to prevent the casing from being distorted and the internal parts from being damaged.

- Install the lift according to the lift specifications before installing Ultra 3D. Check the lift regularly for fixedness and levelness to ensure personal safety and correct measurement. Remove the obstacles around the lift for convenient operation.

- Don’t place Ultra3D on a vibrated object or an oblique surface. Avoid direct sunlight and moisture.

- Avoid splashing water on the surface of Ultra3D, for it may cause permanent damage to the system.

- The targets are major components for wheel alignment, be careful in storage or operation. Clean the dirt with neutral detergent or ethanol.

- Accurate calibration is made during manufacturing, and the design doesn't require calibration work for a few years, install Ultra3D according to the user manual. Do NOT move the column, open or adjust cameras, or else the warranty is expired automatically, and end user will bear the cost of damage.

- Video cameras are high precision parts; the filters shall be kept clean.

- Turn off the power after operation. Check all bolts and parts after maintenance, and tighten the slackened bolts and parts in turn for safety.

- Check the packing list before installing. Do not hesitate to contact Protec Equipment Canada Inc or its distributors for any questions.

# General Safety Instructions

The chassis measurement system may only be used to measure vehicle axles according to specifications.

Only trained professional may operate the system.

Safety equipment may not be removed and/or disabled.

Repairs may only be performed by trained customer service personnel. Arbitrary modifications of the system exclude any liability by Protec Equipment Canada for any resulting damages.

Any work on the electrical installation may only be performed by electricians.

The wheel aligner system may not be operated in explosion- prone surroundings.

The operator must provide appropriate fire protection measures at the measuring platform. In particular, any flammable or self- combusting items (such as cloths soaked in solvents or oil) and fluids, or foreign items and other ignition sources, should not be stored in the tool trolley.

Obligation by the operator to be considerate and avoid negligent acts:

The equipment was designed and constructed with consideration to required harmonized standards, as well as additional technical specifications. It therefore corresponds with the current state of technology and provides the maximum standard in safety during the operation.

The machine safety, however, can only be implemented during the operation, if all of the required steps have been taken. The operator of the machine has the obligation to plan these actions and check their compliance.

The operator must specifically verify that:

• The machine is only used according to specifications.

• The machine is only operated in perfect operational condition and that the safety equipment is routinely inspected as to their operational condition.

• The necessary personal safety equipment for operating, maintenance and repair personnel is available and being worn.

• The operating instructions are always in a legible condition and are completely available at the machine location.

• The machine is only operated, maintained and repaired by qualified and authorized personnel.

• This personnel is instructed routinely in all pertaining questions of work safety and environmental protection, and knows the operating instructions, especially the safety instructions contained therein.

• All safety and warning labels attached to the machine are not removed and are legible.

# Concrete safety instructions and applied symbols

Concrete safety instructions are provided in the following operating instructions which will point out any unavoidable remaining risks during the machine operation. These remaining risks contain hazards for:

Persons

Product and machine

The environment

Basic safety measures during normal operations:

The machine may only be operated by trained and authorized personnel who know the operating instructions and are capable of working with them!

Prior to switching the machine on, check and verify that:

Only authorized personnel are located within the working range of the machine.

No one can be injured when the machine is activated!

Check the machine for visible damages prior to use and verify that it is only operated in perfect condition! Report any problems immediately to the supervisor!

Prior to each operating start, check and verify that all safety equipment operates perfectly!

Basic safety measures during service and maintenance:

Adhere to the inspection and maintenance intervals specified in the operating instructions!

Block access to the work area of the machine to unauthorized personnel prior to performing maintenance or repairs! Attach or set up a warning sign that points out maintenance or repair work!

Pull the power plug prior to any maintenance or repair work or switch off the main switch for the power supply and secure with a lock, if the power supply is installed.

The key to this lock must be in the hands of the person that is completing the maintenance or repair work! Only use perfect load suspension and lifting equipment when replacing heavy machine parts!

Properly dispose of environmentally hazardous lubricants, coolants or cleaning agents!

Working on the electrical equipment:

Repairs on electrical equipment of the machine may only be performed by trained electricians!

Electrical equipment must be routinely inspected!

Re-attach any loose connections!

Immediately replace damaged lines/cables!

Always keep housings of electrical equipment closed! Access is only permitted for authorized personnel with key/tools!

Never spray the housing of electrical equipment with a hose when cleaning!

Observe environmental regulations:

The legal regulations for waste prevention and proper recycling/disposal must be adhered to for all operations on and with the machine.

Especially during installation, repair and maintenance operations, water-polluting materials, such as:

Lubricants and oils - hydraulic oils - coolants.

Solvent-containing cleaning liquids may not pollute the ground or reach the sewage system!!

These materials must be stored, transported, collected and disposed of in suitable containers!

Table of Content

CHAPTER 1  INTRODUCTON	8

1.1 FUNCTION AND FEATURES	8

1.2 TECHNICAL SPECS	8

1.3 WORKING CONDITION REQUIREMENT	8

1.4 WORKING PRINCIPLE	9

CHAPTER 2 HARDWARE	11

2.1 GENERAL ELECTRIC CONTROL UNIT	11

2.1.1 WIRING	11

2.1.2 WORKING PRINCIPLE	12

2.1.3 KEY COMPONENT CONTROL	12

2.2 POWER SUPPLY	13

2.2.1 POWER SUPPLY MAP	13

2.2.2 FUNCTION EXPLANATION	13

2.2.3 WIRING	14

2.3 SWITCH POWER SUPPLY	14

2.3.1 FUNCTION	14

2.3.2 SPECS	14

2.4 CONTROL MAINBOARD PCB	15

2.5 LED PCB	16

2.5.1 FUNCTION	16

2.6 CAMERA ASSEMBLY	16

2.6.1 STRUCTURE	17

2.6.2 FUNCTION	17

2.7 PC HOST	18

2.7.1 PC ON-BOARD PORTS CONNECTION	18

2.7.2 FUNCTION	18

CHAPTER 3  SOFTWARE	11

3.1 OPERATION SYSTEM	19

3.1.1 INTRODUCTION	19

3.1.2 SOFTWARE DISC	19

3.2.4 INSTALLATION	19

ChAPTER4  sERVICE	19

4.1 pc RELATED	20

4.1.1 COMPUTER CAN NOT BOOT	20

4.1.2 CAN NOT ENTER WIN 7 DESKTOP	20

4.1.3 MOUSE/KEYBOARD NOT FUNCTIONAL	20

4.1.4 PRINTER NOT FUNCTIONAL	20

4.1.5 CAN NOT RUN THE WHEEL ALIGNER SOFTWARE	20

4.2 VEHICLE MEASUREMENT RELATED	20

4.2.1 WHEN TURN THE STEERING WHEEL, BLOCK REAR TARGET, BUT THERE’S NO ERROR PROMPT	20

4.2.2 WHEN TURN THE STEERING WHEEL, TARGET BLOCKED PROMPTED	21

4.2.3 WHEN TURN THE STEERING WHEEL AND GREEN BALL SHOWS, THEN CAMERA BLOCKED.	21

4.3.4 THE MIN TURN ANGLE OF FL AND FR ARE DIFFERENT.	21

4.2.5 AT TARGET MONITORING SCREEN, SOME TARGETS NOT IN RANGE	21

cHAPTER 5 PARTS LIST	20

5.1 MAIN COMPONENTS	21

5.2 COLUMN ASSEMBLY PARTS LIST(AUTO-FOCUS）	22

5.4 CAMERA BAR ASSEMBLY PARTS LIST	24

5.5 CABINET ASSEMBLY PARTS LIST	25

5.6 GENERIC PARTS LIST	26

# Chapter 1  Introduction

## 1. 4  Function and feature

All new three dimension computer visual measurement: adopted high performance camera to automatically detect the alignment parameter. The equipment was calibrated at production, does not need on-site calibration at installation.

Complete parameter measurement: Capable of test of front/rear toe-in, front/rear camber, thrust angle, caster, SAI/Kingpin, wheelbase, track (thread) etc. Can measure track width, wheelbase, etc. as show below:

Electric component free target: no electric component or wiring on the target, which ensure the equipment to be more convenient and durable.

Extremely simplified test procedure.

Complete database: More than 20000 records of vehicle all over the world, and user can add data at will.

Historical data storage for client management.

Vehicle chassis adjustment indication picture

Real-time help system.

Data backup/restore, and update function.

## 1. 2 Tech Specs

| alignment parameter | Accuracy | Range | Max measureable Range |
| --- | --- | --- | --- |
| Camber | ±2´ | ±2° | ±20° |
| Toe | ±2´ | ±2° | ±20° |
| Caster | ±4´ | ±10° | ±20° |
| Steering Axle Inclination | ±6´ | ±15° | ±20° |
| Thrust Angle | ±2´ | ±2° | ±10° |

Display Accuracy: 0. 01˚ / 1’ / 0. 1mm / 0. 1inch

Caution:

- LAUNCH EQUIPMENT CANADA INC. preserves the right to change design without prior notification.

- The measure range can only be assured when operate the wheel aligner according to the user manual.

## 1. 3 Requirements on Surroundings

Ambient temperature:0～50℃

Relative humidity:≤85%

Light condition: No direct Infrared light to the targets

lift platform height difference: front/end height difference < 2mm

Appendix “site check list before installation  "

Ultra3D+ Wheel Aligner

| Check List | Requirement | Actually Measured Result | Rating |
| --- | --- | --- | --- |
| Installation Height of Column ( Distance from ground to top end of the column) | 2810mm | 2750mm |  |
| Alignment Platform Height ( Distance from ground to Turntable Surface) | 0-1600mm | There might be up to 100mm difference depends on the size of wheel, wheel base, distance from left to right post(4 post lift) |  |
| Column Standard Distance(Distance from center of turntable to Column front surface) | 2200mm | -300mm to 300mm tolerance, difference in distance will result in change in measurement height. |  |
| Platform front/end height difference | <2mm | Big height difference will result in difficulty in doing pushing compensation. |  |
| Power Supply | AC 220V/110V 8A |  |  |

## 1. 4 Working Principle

Ultra 3D(+) wheel aligner working principle is as show in figure 1. The entire system can be dividing into two categories: data acquisition and data processing.

Data acquisition category consists of 2 high definition cameras and 4 targets. Left and right side camera get target image and send to data processing category. Target was mounted onto the wheel via clamps.

Data processing category is the core component of Ultra 3D(+) wheel aligner, consist of computer system, power supply system and interface. The function is to realize operator’s instruction, automatically guide the measurement, calculate data and display together with manufacturer data, at the same time, guide the operator to do adjustment on the vehicle. Finally, print out the report.

Since Ultra3D(+) wheel alignment system need to compare tested data with manufacturer data, and provide guidance of adjustment, database is very important to provide reference data. Ultra3D(+) wheel aligner database covers over 20000 records of vehicle data worldwide. At the same time, Ultra3D(+) wheel aligner system provide function for operator to input and save customized data.

# Chapter 2  Hardware

## 2. 1 Electronic Control

### 2. 1. 1 Electronic Control Wiring Connection

| Ultra3D(+) Electronic Control Wiring Connection |
| --- |
| 1. 3 Meter power cable | 2. Power plug | 3. Fuse plug |
| 4. Power Switch Cable | 5. Power switch | 6. Switch power |
| 7. Switch power in-line cable | 8. Power plug(6 pack) | 9. Camera(2 units) |
| 10. Camera data cable (2 pcs) | 11. LED Board (2 pcs) | 12. LED Board power cable (2 pcs) |
| 13. upper limit switch power cable | 14. limit switch | 15. lower limit switch power cable |
| 16. Control board PCA | 17. Low voltage power cable | 18. Motor |
| 19. Data bus |  |  |

### 2. 1. 2  Working Principle

Power Supply was lead into the system via 2 and 1; 3 was mounted inside 2, in order to offer over voltage protection; then connect to 5 via 4, to control the power supply to 8, 8 provide power source to computer host and monitor; at the mean time, 5 also control the power source to 6, which convert the power source to DC12V, and provide to 16 via 17.

16 drives 18 according to the signal passed from computer host; 16 also capture status of 14 via 13 and 15 then feedback to computer host. 16 also control 11 via 12. 11 provide light source for the targets mounted on 4 wheels, and captured by 9 for data collection, and transfer to 16 via 10. Then transfer to computer host via 19.

Computer host will calculate the collected data transferred, and show the data onto the monitor.

### 2. 1. 3 Control diagram

Ultra3D(+) Control Diagram

## 2. 2.   Power Socket

| Front | Rear |
| --- | --- |

### 2. 2. 1 diagram

| Fuse Socket is below the power socket | Fuse Socket uncounted | Fuse in the fuse socket |
| --- | --- | --- |

### 2. 2. 4 Function

- There are 2 fuses in the fuse socket, 1 in use and another is spare.

### 2. 2. 3 Wiring

Wiring diagram

## 2. 3 Switch power

### 2. 3. 1 Function

### 2. 3. 4 Function

Switch power input AC220V±10%, output DC12V. 0±0. 1V, output voltage could be adjusted if it’s off the standard range.

Switch power transit AC220V into DC12V for Control board PCA.

## 2. 4 Control board PCA

| 1) diagram |
| --- |
| Camera(Right) USB port | Camera(left) USB port | LED board PCA (right) power source |
| LED board PCA (left) power source | upper limit switch power source | lower limit switch power source |
| Motor power source | Switch power inlet port | Data bus port |
| Manual rise/drop switch |  |  |

## 2. 5 LED Board PCA

Front

3 LEDs consist 1 group

every group of LED is equipped a limit resistor

### 2. 5. Computer Related 1 Function

- There are 96 pcs of 850nm LED on every LED board PCA;

- LEDs are grouped at the basis of 3 pcs per ground, total 32 groups.

- 5V power supply was provided via control board PCA.

- LED board PCA provides enough light to reflect on the targets and collect by the camera.

## 2.  Camera

Front

Camera was controlled via USB from the control PCA.

### 2. 6. 1 diagram

| Side view of Camera |
| --- |
| 1. Filter | 2. Focus Ring | 3. Focus Ring position indicator |
| 4. Aperture position indicator | 5. Aperture | 6. Camera |
| Video Camera consists of filter, lens (2, 3, 4, 5, 6, and 7) and camera. |
| Camera |
| 1. Filter press cover | 2. Filter | 3. Filter socket |
| 4. Lens | 5. Camera | 1,2,3 consist Filter assembly |

### 2. 6. 2 Function

- Image was captured by the camera after get rid of noise.

- Camera transfers the image to computer host via control board PCA.

- The camera and lens had been adjusted to the best position, shall not adjust the camera without factory approval.

## 2. 7 Computer Host

### 2. 7. 1 Rear interface

|  | 1. Power socket |
| --- | --- |
|  | 2. voltage switch |
|  | 3. Speaker socket |
|  | 4. Ethernet socket |
|  | 5. USB Sockets |
|  | 6. Monitor Socket |

### 2. 7. 2 Function

- Computer Host connect to the control board PCA

- Camera transfers the image to computer host via control board PCA.

- Realize display and print function.

# Chapter 3 Software

## 3. 1 Operation System

### 3. 1. 1 Operation System Requirement

- Windows 7 Pro/Ultimate 32 bit version

### 3. 1. 2 Software CD

- Yes

In case the data jumps on the display during test, clean the targets use a soft cotton cloth impregnated with an appropriate amount of neutral detergent or ethanol.

### 3. 2. 4 Key points of installation & adjustment

#### 3. 2. 4. 1 Ultra3D(+) installation position

| Ultra3D(+) installation position |
| --- |
|  | A: Center line of vehicle lift runways | H0: Calibration Height |
|  | B: Column front surface | Hmin: minimal measurement height |
|  | C: center line of turntables | Hmax: Maximam measurement height |
|  | D: Distance from column to turntables |  |
| Standard calibration height and installation distance. |
| D | H0 | Hmin | Hmax |
| 2200 | 1020 | 920 | 1120 |

# Chapter 4   Troubleshooting

## 4. 1 Computer Operation

### 4. 1. 1 Computer can not boot

Check the power supply of computer.

Check if the power button is clicked on both the computer host and monitor, whether the indication LED is flashing.

Check the brightness and contract of the monitor.

### 4. 1. 2 Can not enter WINDOWS 7 desktop

Computer boot file missing.

BIOS error.

Hardware failure.

### 4. 1. 3 Mouse/keyboard not functional

Mouse/keyboard connection to the computer host is faulty.

Mouse/Keyboard not compatible with computer host

Mouse/Keyboard faulty.

### 4. 1. 4 Printer not functional

Check power supply of print, signal cable connection to computer host, and if the print is on linked mode.

Check installation and setting of Driver for printer.

Check if the computer is virus affected.

### 4. 1. 5 Can not run wheel aligner software

Software core file missing.

Registry error.

## 4. 2 Standard measurement

### 4. 2. When turn steering wheel, there’s no camera/target block prompt when block rear targets.

This is normal. won’t affect the measurement result.

### 4. 2. When turn steering wheel, prompts camera block.

Stop turn the steering wheel, clear the block, then continue turning the steering wheel.

### 4. 2. When turn steering wheel, and the green ball shows, prompts camera block.

Turn the steering wheel back to the green ball position and continue caster swing test.

### 4. 3. 4. after wheel alignment, vehicle front wheel max turn angle different from left to right. Why?

This is normally caused by incorrect joint position of steering wheel and steering axis. When adjust chassis, the data is collected assume the steering wheel is centered. Might can correct the joint position and do alignment work again.

### 4. 2. 5 at target monitor page, some of the targets are not in the image.

# Check if the missing targets are mounted on the wheels, if there’s anything blocking the targets, if the LED board PCA failed to be on.

# Chapter 5  Parts List

## 5.1 Main Components

| index | Code | Name | Qty | picture | remark |
| --- | --- | --- | --- | --- | --- |
| 1 | LZ01 | Column Assembly | 1 |  | Ultra3D |
| 2 | LZ02 | Column Assembly | 1 |  | Ultra3D+ |
| 3 | HL01 | Camera Bar | 1 |  |  |

## 5.2 Column Component List（Ultra3D+）

| index | code | name | qty | picture | remark |
| --- | --- | --- | --- | --- | --- |
| 1 | LZ0201 | Top cover | 1 |  |  |
| 2 | LZ0202 | Column | 1 |  |  |
| 3 | LZ0203 | Lifting assembly | 1 |  |  |
| 4 | LZ0204 | Column base | 1 |  |  |
| 5 | LZ0205 | Upper rail |  |  |  |
| 6 | LZ0206 | Steel cable assembly | 1 |  |  |
| 7 | LZ0207 | Limit block | 2 |  |  |
| 8 | LZ0208 | Roller rack | 1 |  |  |
| 9 | LZ0209 | Weight balance unit | 1 |  |  |
| 10 | LZ020301 | Motor | 1 |  |  |
| 11 | LZ020302 | Control board PCA | 1 |  |  |
| 12 | LZ020303 | Limit switch | 2 |  |  |
| 13 | LZ020304 | Roller | 1 |  |  |
| 14 | LZ020305 | Width resistor | 4 |  |  |
| 15 | LZ020306 | Motor rack | 1 |  |  |
| 16 | LZ020307 | Control board PCA mounting screw（M3*10+6mm） | 4 |  |  |
| 17 | LZ020308 | Upper limit switch power cable | 1 |  |  |
| 18 | LZ020309 | Lower limit switch power cable | 1 |  |  |
| 19 | BZ0601 | M16*100 | 4 |  |  |

## 5.3 Column Component list（Ultra3D）

| index | code | name | qty | picture | remark |
| --- | --- | --- | --- | --- | --- |
| 1 | LZ0101 | Top cover | 1 |  |  |
| 2 | LZ0102 | column | 1 |  |  |
| 3 | LZ0103 | Switch power | 1 |  |  |
| 4 | LZ0104 | Column base | 1 |  |  |
| 5 | LZ010301 | Power box (lower) | 1 |  |  |
| 6 | LZ010302 | Power box (upper) | 1 |  |  |
| 7 | LZ010303 | Switch power (AC110~220V in, DC12V out) | 1 |  |  |
| 8 | LZ010304 | 4 power sockets | 1 |  |  |
| 19 | BZ0601 | M16*100 | 4 |  |  |

## 5.4 Camera Bar Assembly component list

| index | code | name | qty | picture | remark |
| --- | --- | --- | --- | --- | --- |
| 1 | HL0101 | Camera Assembly | 2 |  |  |
| 2 | HL0102 | Camera front cover | 2 |  |  |
| 3 | HL0103 | Camera rear cover | 1 |  |  |
| 4 | HL0104 | Lateral bar | 1 |  |  |
| 5 | HL0105 | Lateral mounting shelf | 1 |  |  |
| 6 | HL0106 | Wiring sealing | 4 |  |  |
| 7 | HL010101 | LED board PCA | 2 |  |  |
| 8 | HL010102 | LED board PCA back cover | 2 |  |  |
| 9 | HL010103 | Camera rack | 2 |  |  |
| 10 | HL010104 | camera | 2 |  |  |
| 11 | HL010105 | Data cable | 2 |  |  |
| 12 | HL010106 | lens | 2 |  |  |
| 13 | HL010107 | Filter press cover | 2 |  |  |
| 14 | HL010108 | filter | 2 |  |  |
| 15 | HL010109 | Filter base | 2 |  |  |
| 16 | HL010110 | LED board PCA mounting screw（M3*20+6mm） | 8 |  |  |

## 5.5 Cabinet Component List

| index | code | name | qty | picture | remark |
| --- | --- | --- | --- | --- | --- |
| 1 | JG0201 | Cabinet | 1 |  |  |
| 2 | JG0202 | Computer Host | 1 |  |  |
| 3 | JG0203 | Monitor | 1 |  |  |
| 4 | JG0204 | Printer | 1 |  |  |
| 5 | JG0205 | Switch Power | 1 |  |  |
| 6 | JG0206 | 6pack power socket | 1 |  |  |
| 7 | JG0207 | Mini speaker | 1 |  |  |
| 8 | JG0208 | Data bus | 1 |  |  |
| 9 | JG0209 | Low voltage power cable | 1 |  |  |
| 10 | JG0210 | Switch power cable | 1 |  |  |
| 11 | JG0211 | Transit cable | 1 |  |  |

## 5.6 Generic Parts List

| Index | code | name | qty | picture | remark |
| --- | --- | --- | --- | --- | --- |
| 1 | TY0101 | Power cable | 1 |  |  |
| 2 | TY0201 | Power socket | 1 |  |  |
| 3 | TY0301 | Power Switch | 1 |  |  |
| 4 | TY0401 | Clamp holder | 4 |  |  |
| 5 | TY0501 | Clamp(24 inch) | 4 |  |  |
| 6 | TY0601 | FL target | 1 |  |  |
| 7 | TY0602 | FR target | 1 |  |  |
| 8 | TY0603 | RL target | 1 |  |  |
| 9 | TY0604 | RR target | 1 |  |  |
| 10 | TY0701 | Steering wheel holder | 1 |  |  |
| 11 | TY0801 | Brake pedal depressor | 1 |  |  |
| 12 | TY0901 | LED PCA Power cable (L) | 1 |  |  |
| 13 | TY0902 | LEDPCA Power Cable(R) | 1 |  |  |

# Text boxes

Target(L)

Target(R)

Camera(R)

Camera(L)

Monitor

Printer

Keyboard, mouse

Computer

1

2

3

5

4

5

76

5

4

3

2

1

6

5

4

3

2

1

5

4

3

2

1

10

9

8

7

6

Voltage adjustment

DC12V

DC V+

DC V-

GND

AC V-

AC V+

220V

Monitor

Computer Host

Motor

Limit switch

Control board PCA

Switch power

Camera(Left)

LED PCA (Left)

LED PCA (Right)

Camera(Right)

1

2

3

4

5

6

7

8

9

10

11

12

13

14

15

16

17

188

19